## Slide 1: Inverse Problems, Constraint Satisfaction, Reversible Logic, Invertible Logic and Grover Quantum Oracles for Practical Problems
Marek Perkowski
Department of Electrical and Computer Engineering
Portland State University
Friday, July 10th 2020

## Slide 2: What is an Oracle?
Technical aspects can be found in the paper and its references
Here I want to concentrate on fundamental ideas and our philosophy
So that everybody can start using these ideas in their related areas of research

## Slide 3
a b
c d
1
1
1
1
1
1
1
1
1
1
Classical Boolean Circuits propagate signals only from inputs to outputs
1
1
1
1
1
1
1
A Boolean function with one output we will call an Oracle
Oracle is a fundamental concept in Grover Algorithm, which is the famous quantum algorithm with many applications.
Propagating signal through a combinational circuit from input to output is called evaluation of the oracle.
With input combination a=1,b=1,c=1,d=1 we need to propagate signal only once through this oracle to obtain value “1” on output.
What is an Oracle in Quantum Computing?

## Slide 4: The Essence of Quantum Algorithm of Grover

## Slide 5: A gold ball in a box or a miracle of a quantum algorithm
We have one gold ball in a black box and 99 black balls.
We do not know anything about what is inside the box, other that there is a gold ball inside.
We reach to the box, if the ball is gold we are happy, otherwise we remove the black ball from the box and reach again.
We repeat this until we find the gold ball.
In the best case we find the ball in the first attempt, in the worst case - in the attempt number 100.
On average we need to reach 50 times to the box.
In quantum we need to reach only 100 =10 times to find the gold ball.
Why it is so?
The answer is quantum superposition or quantum parallelism

## Slide 6: Classical Gold Ball (illustrated with 4 balls)
1
2
3
4
3
We use a sequential search algorithm in a non-organized (uninformed) database (space)
Quantum Gold Ball
1
We use a parallel search algorithm using superposition in Hilbert Space
2
4
4 processors
Black balls are shrinked
Gold ball grows
Initial quantum state
3
Processor for ball 1
Processor for ball 2
Processor for ball 3
Processor for ball 4
First iteration of Grover Loop
Second iteration of Grover Loop
time
Measurement
The winner is
Notes: Every potential solution has a hypothetical processor

## Slide 7
Special Controller
Classical Computer
Initialization
Calculations
Measurement
Problem specific data
Quantum states in Hilbert Space
Sequential pulses that control qubit transformations
1000 qubits = 21000 “processors”
Quantum states in Hilbert Space
Classical binary States
Grey Rectangle here is a Hilbert Space
Boolean Algebra
Quantum Mechanics
Modern Quantum Computer is a Hybrid Machine

## Slide 8: Conclusion on Grover
Power of quantum computing is in very high parallelism.
Having 2 particles is equivalent to having 4 computers.
Having n particles means that we have a parallel computer with 2n processors.
Now there are universal quantum computers with 100 qubits (particles).
This means 2100 processors working in parallel.
But this parallelism is not for all problems.
Let us go back to oracles

## Slide 9
Now the gold ball is a “1”, the black balls are the “0”.
I want to find for which combination of input a,b,c,d the output is 1.
I do not know what is the function, I can only guess the inputs and check the output.
This is like a testing problem.
I give one minterm at a time.
In the worst case I need to test 16 minterms.
In the best case I need to test 1 minterm, on average I need 8 minterms.
Grover will find the solution in 16 = 4 tests.
1
0
0
0
0
False minterm
True minterm
0
0
0
0
0
0
0
0
0
0
0
Boolean Function formulation of the Gold Ball problem
Assume that the oracle circuit of function F2 is just a tree of two-input AND gates with 64 inputs in total.
To find the 1 of function, the oracle in classical logic would be evaluated 264 number of times.
Grover Algorithm would evaluate the oracle “only” 2^ (64/2) = 232 times which may be also not practical.
However, in Invertible logic in which one propagates the signals from output to inputs, the Invertible Logic method would need only one evaluation of the oracle realized with invertible gates
a,b\c,d

## Slide 10: Inverse Problems

## Slide 11: Inverse Problems for functions
a b c d e f g h
1 2 3 4 5 6
What are all letters that map to number k ?
Inverse Problems for relations
RELATION
a b c d e f g h
1 2 3 4 5 6
What are all letters that map to number k ?
Is characteristic function satisfied?
a
b
c
1
2
3
d
4
5
e
f
6
g
h
domain
co-domain
F=1111
Characteristic function
Notes: Domain codomain

## Slide 12: Examples of Inverse Problems solved by Invertible Logic
adder
1
2
?
adder
1
2
3
adder
?
?
3
adder
0
3
3
adder
1
2
3
adder
0
3
3
……

## Slide 13: … but also…. Generalized Inverse Problems
adder
1
?
3
adder
1
2
3
multiplier
?
?
15
multiplier
5
3
15
multiplier
3
5
15
multiplier
15
15
1
……
Cryptography
Quantum cryptography
Post-quantum cryptography
Integer Factorization
Signal propagation in all directions
Notes: Some inputs , some outputs

## Slide 14: Reversible Logic

## Slide 15: Notation for Classical Boolean Logic Gates and Invertible Logic Gates
a
a
a
b
ab
a
b
a * b
INVERTER
AND
EXOR
OR
a
b
a + b
These gates propagate from inputs to outputs

## Slide 16: Notation for Reversible Logic Gates
a
a
a
b
a
ab
a
b
a
abc
b
c
a
a
a
Inverter
a
b
ab
Controlled-NOT or Feynman Gate
a
c
abc
.
.
a
b
b
.
Controlled-Controlled-NOT or Toffoli Gate
These gates are in reversible logic. Propagate from input to output or from output to input.
In quantum realization they allow for superposition and entanglement

## Slide 17: Reversible Circuits from Reversible Gates
Truth Tables
Schematic Diagram
These are reversible functions, one-to-one mappings or permutations.
These are also reversible gates from which reversible circuits are composed.
This is an example of a circuit created from reversible gates without ancilla bits.
The corresponding function is reversible.

## Slide 18
Hadamard Transform
Single qubit
H
H
H
Parallel connection of two Hadamard gates is calculated by Kronecker Product (tensor product)

1 | 1 | 1 | 1
1 | -1 | 1 | -1
1 | 1 | -1 | -1
1 | -1 | -1 | 1
1/2
=
=
Here I calculated Kronecker product of two Hadamards

## Slide 19
Hadamard Transform
H
H
|0
|0
1/2|00+1/2|01+1/2|10+1/2|11
After vector of Hadamards we have equal superposition of all states from my problem space

## Slide 20: Invertible Logic

## Slide 21
1
a b
c d
1
1
1
1
1
1
1
1
1
1
What is Invertible Logic?
Invertible Logic algebraically is exactly the same as classical Boolean Logic.
The only difference is that the invertible logic CIRCUIT can just propagate signals:
  From inputs to outputs
  From outputs to inputs
  From any subset of inputs and outputs and internal signals in any direction.
Invented by Professor Datta from Purdue as a result of investigation of Deep Recursive Neural Nets.
So now, in only one evaluation of oracle we find the solution a=1,b=1, c=1,d=1. F = abcd.
For n=64 variables the quantum Grover Algorithm will need to evaluate the Oracle 232 times. NOT GOOD.
Invertible Logic will find solution in only one evaluation of oracle.
This is an example of Inverse Problem

## Slide 22: Few important points
The creator of the oracle does not know the function like we can see it in a Karnaugh Map.
He can create the oracle as a circuit without knowing the function.
This oracle can be evaluated using:
  A classical Boolean Oracle
  A Quantum Oracle
  An Invertible Logic Oracle.

## Slide 23: How Invertible Logic works?
1
1
1
1
0
0
0
0
0
0
1
0
1
0
Deterministic propagation
Non-deterministic propagation
Similarly we can analyze any Boolean Gate or block such as adder

## Slide 24: How Invertible Logic works?
Invertible Logic solves Inverse Problems.
  Graph Coloring
  Integer Factorization
  Cryptology
  Bitcoin
  Puzzles
  Electronic Design Automation
  Inverse Kinematics
Fig. 16
And every problem described by an oracle
Invertible Logic is a general concept
It is in principle not related to any technology

## Slide 25: A Dream of Universal Method “to Solve All Problems”

## Slide 26: Old History of Universal Method for Problem Solving
Raymond Lullus (1232-1316)
Rene Descartes (1596-1650)
George Boole (1815-1864)
Stanley Petrick (1931-2006)
Claude Shannon (1916-2001)
Pyne and McCluskey
Universal Method
Mappings, syllogisms, graphs, MV logic
Every Problem can be reduced to a single Algebraic Equation
Every Problem can be reduced to a single Boolean Equation
Many, many papers
SAT solvers and NP theory
Oracles
The research presented in this lecture
Linear algebra
Symbols, diagrams, relations
Boolean algebra
Every Problem can be reduced to solving an oracle
Grover

## Slide 27: George Boole said:
Describe a problem by a set of simple logic equations.
Convert the set of these equations to a single logic equation.
Solve this equation to get all answers.
“universal method” to solve logic problems

## Slide 28: History and Ideas
Hopfield Nets
Boltzmann Machines
Deep Learning Boltzmann Machines
Invertible Logic
Magnetic Spin Technology
Inverse Problems
Constraints Satisfaction Problems
Oracles
Generalized Oracles
Optimization Problems
PSU Methodology to Solve Problems
Perkowski 1981-2020
Classical Boolean Logic
Grover Algorithm
Quantum Walk
Quantum domain
Prolog Software
Quantum Invertible Logic
CMOS
FPGA
Magnetic Spins
Other non-quantum nanotechnologies

## Slide 29: What is my achievement?
People who work on Invertible Logic do not have a methodology to develop oracles.
We combine our methods of classical, reversible and invertible logic to build a very large class of oracles and reduce problems from various areas to building oracles.
Optimization Problems are reduced to sequence of oracles with modified constraints.

## Slide 30: Constraint Satisfaction Problems

## Slide 31: Constraint Satisfaction
Given is a set of arithmetic, Boolean, Predicate and other constraints on a set of variables.
Find all vectors of values of variables that satisfy all constraints
Given is a set of arithmetic, Boolean, Predicate and other constraints on a set of variables.
Find all vectors of values of variables that satisfy as many as possible constraints
Given
  is a set of arithmetic, Boolean, Predicate and other constraints on a set of variables
  Cost function.
Find all vectors of values of variables that satisfy all constraints AND optimize the cost function
Optimization

## Slide 32: Constraint Satisfaction Problems
Graph Coloring
Maximum Clique
Maximum Independent Set
SAT and MAX-SAT
8 Queens
Logic Puzzles
Integer Linear Programming
Partition Calculus Problems
POS to SOP conversion
FPRM Minimization
Two-level logic minimization
Finite State Machine Minimization
FSM encoding
Concurrent encoding and minimization of FSM
Ashenhurst-Curtis Decomposition of Logic functions.
Minimum Set of Support
Rule Minimization
Binate Covering
Unate Covering
Logic methods of Machine Learning.
Generalized Traveling Salesman
Generalized Knapsack
Shortest Path and several robot planning tasks
Yiwei Li
Sharavana Kumar, visitor from India
Perkowski
Peng Gao
Wei Zhang, visitor from China
Wenjun Hou, high school
Jacob Viertel from Germany
Test generation
Cryptography
Logistic problems
Non-linear Algebraic equations

## Slide 33: Example of CSP – Graph Coloring
This graph colored with one color
These two graphs need two colors
This graph G1 needs three colors
Oracle for coloring graph G1
1
2
3
a
b
c
Chromatic number of our graph is 3 because we cannot color it with 2 colors a and b

## Slide 34: Example of CSP – Graph Coloring
Oracle for coloring graph G1
1
2
3
a
b
c
Our methodology creates such general oracle from the specification
Standard Boolean Gates
Quantum Circuit
FPGA
Reversible Logic
Backtracking Simulator in PROLOG
Standard Boolean Gates converted to Hamiltonians
FPGA with Random Number Generators
IBM quantum computer
Quantum Simulator
Linear Programming
Our Methodology – what we do with the oracle?

## Slide 35: We think about gates and blocks as characteristic functions or relations
Think about a gate (a block, a Hamiltonian) as a little processor that likes to minimize its energy
1
1
0
I like it. I have minimum energy, I am happy, let us keep my state this way
1
1
0
I like it. I have minimum energy, I am happy, let us keep my state this way
1
1
1
I hate it. I do not have minimum energy. I need to change signals.
1
1
0
0
1
1
I am happy again

## Slide 36: Methodology to solve Constraint Satisfaction Problems and Optimization Problems based on Generalized Oracles

## Slide 37
Bottom-up rather than Top-Down
Gates and blocks, not Unitary or Permutative Matrices
Use libraries
Blocks: logic, arithmetic, predicates, problem-specific (like controlled counters)
Subset-of-set, versus permutative, versus mappings, versus combinations without repetitions, etc.
Encoding of data (short codes, one-hot, thermometer, etc)
Calculate abstract complexity such as number of iterations of oracle.
Calculate detailed complexity in terms of number of qubits, number of gates, number of pulses, etc.
Reusing of problem reductions, design tricks and verified blocks
Special synthesis algorithms for symmetric functions, ESOPs, PSOE, factorized forms, adders, controlled-adders, constant-multipliers, comparators, etc. = we use engineering design practices.
Using QSHARP, QISKIT, QUIPPER
Using Prolog for Oracle Simulation.
Ternary logic.
Key points of our methodology

## Slide 38: Grover Algorithm and Quantum Oracles

## Slide 39
Second Example
oracle
Inversion by mean
One repetition of GroverLoop for 2-SAT Problem, full circuit has two
0
1
2
3
4
5
6
7
Weight 1
Weight 2
Weight 4
Weight 8
Weight 16
2+1=3
16+4+2+1=23
16+8+4+2+1=31
4+2+1=7
Numbers for solutions
Problem has 4 solutions, as shown in Truth Table 2.2.
Remember weights

## Slide 40
Phase of our 4 solutions is different
Magnitude of our 4 solutions is amplified
32
After vector of Hadamards all solutions are equally probable
After oracle solutions are in negative phase
1/2|00+1/2|01+1/2|10+1/2|11
This would be for 2 variables
Superposition
RESULTS OF FIRST ITERATION

## Slide 41
Magnitude of our 4 solutions is amplified

## Slide 42: Let us compare states after first and second iteration
3
7
31
23
Even measuring now the probability of finding one of solutions is high
Measuring after two iterations the probability of measuring one of solutions is very high

## Slide 43: Grover for Graph Coloring

## Slide 44
A Simple Graph Coloring Problem
2
1
3
4
Two wires for color of node 1
Two wires for color of node 2
Two wires for color of node 3
Two wires for color of node 4

Gives “1” when nodes 1 and 2 have different colors


12
13
23

24

34
Value 1 for good coloring
We need to give all possible colors here
F(x)

## Slide 45
Sequential Generator and Oracle for Graph Coloring
≠
Gives “1” when nodes 1 and 2 have different colors
≠
≠
12
1  3
2  3
≠
2  4
≠
3  4
Value 1 for good coloring
We need to give all possible colors here
F(x)
Counter with 2 8 states
Sequential Generator
Oracle
Discuss naïve non-quantum circuit with a full counter of minterms

## Slide 46
Hypothetical
Parallel
Computer
for Graph Coloring
and
28 combinational
oracles
≠
≠
≠
1≠2
1≠3
2≠3
≠
2≠4
≠
3≠4
Value 1 for good coloring
F(x)
Oracle number 0
≠
≠
≠
1≠2
1≠3
2≠3
≠
2≠4
≠
3≠4
Value 1 for good coloring
F(x)
Oracle number 2 8
00000000
11111111
28 combinational
oracles

## Slide 47: In case of quantum circuit, combinational parallelism is realized by superposition of states.
Circuit calculates on 2n states at the same time

## Slide 48
Simple Graph Coloring Problem
≠
≠
≠
≠
≠
Value 1 for good coloring
We need to give all possible colors here
H
H
H
H
H
Give Hadamard for each wire to get superposition of all state, which means the set of all colorings
|0>
|0>
|0>
Now we will generate whole Kmap at once using quantum properties - Hadamard
f(x)
Now we have quantum oracle with quantum reversible gates
|0>
|0>
……
12
1  3
2  3
2  4
3  4
F(x)

## Slide 49: From Classical to Quantum Oracles
Non-reversible,
Built from standard gates like AND,OR,EXOR, NOT.
Calculate candidates sequentially
Reversible,
Built from standard quantum gates like Toffoli, CNOT, NOT.
Calculate candidates in parallel, thanks to quantum superposition
Classical Oracle
Quantum Oracle

## Slide 50: Reducing Optimization Problems to Decision Problems with Modified Oracles

## Slide 51: Grover for Minimum Set of Support Problem
Hybrid Classical-Quantum Computer creates a sequence of modified oracles for Grover
IDEA

## Slide 52: Example: Minimum Set of Support
Minimum Set of Support Problem
Machine Learning
Logic Synthesis
Unate Covering
Binate Covering
Rule Simplification
ACD Decomposition
Test Minimization
POS SOP conversion
SOP Minimization
Petrick Function
Fundamental Algorithms

## Slide 53: Example: Minimum Set of Support
Compare evey true minterm with every false minterm
Karnaugh Map of an incomplete function of 4 variables a,b,c,d. (Mathematically a relation)
From Relational Specification to Set of simple Boolean Equations
ab\cd

## Slide 54: From Individual Equations to a single equation
(a+b).(a+c+d).(a+d).(a+c+d).(a+b).(a+b+c).(a+d)
.(a+b+c).(a+b)
(a+b).(a+d)
Local Equations of Boole
Single Equation of Boole
Using Laws of Boolean Algebra
Oracle
a + bd
POS
SOP
solution
QUANTUM
CLASSICAL

## Slide 55: Encoding and explanation of Grover Oracle for this problem
ab\cd
This cell 1000 is encoding of solution a
(a+b)
0
0
0
0
0
0
a = 1000
b = 0100
c = 0010
d = 0001
ab = 1100
acd = 1011
ENCODING
(a+b).(a+d)
Oracle
a + bd
POS
SOP
ab\cd
Solution a
Solution bd
0
0
0
0
0
0
(a+d)
1
1
1
1
1
1
1
1
1
1
Finding solution a we want to exclude all included in a,
such as ab, ac, abc, abcd
Idea of modifying oracles

## Slide 56: Grover Oracle for all solutions to this problem
(a+b).(a+d)  0 = (a+b).(a+d)
a
b
c
d
0
0
0
a
a b  0
(a+b)
(a+d)
This oracle would find all solutions to problem but most of them would be non-minimal
Use De Morgan Rule
a = 1000
b = 0100
c = 0010
d = 0001
ab = 1100
acd = 1011
ENCODING

## Slide 57: First Grover Oracle for this problem
Set threshold to 1
ab\cd
Solution a
Solution bd
We find solution a with the cost of 1
0
0
0
0
0
0
Controlled adder of 1
Final oracle output

## Slide 58: First Grover Oracle for this problem
Set threshold to 1
We find solution a with the cost of 1
We remove all solutions included in a, such as ab, ac, abc, etc
ab\cd
Solution a
Solution bd
0
0
0
0
0
0
0 0 0 0
0 0 0 0
Final oracle output

## Slide 59: Second Grover Oracle for this problem
|1
We remove solution a from the set of solutions
Block B
ab\cd
Solution a
Solution bd
Set threshold to 2
1 1
0
0
0
0
Final oracle output

## Slide 60: Third Grover Oracle for this problem
ab\cd
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
There is no solution
Grover gives something random, every time different.
We can verify or we can run earlier Quantum Counting to count number of solutions

## Slide 61: Invertible Quantum
Quantum Grover
Classical FPGA
Invertible FPGA
Spin and other nano-technologies
Quantum Hopfield Neural Network -based
Small QHNN
Small QHNN
Small QHNN
The idea of Generalized Oracle is central to all these approaches

## Slide 62: Conclusions
Presented approach allows to solve all Constraint Satisfaction Problems.
Optimization problems are solved by sequence of CSP with modified oracles.
Oracles can be built in several technologies:
  FPGA,
  magnetic spins
  quantum.
Quantum oracles use reversible logic.
Invertible oracles use invertible logic.
In FPGA we can model both classical and invertible logic oracles.

## Slide 63: Conclusions (cont)
When FPGA is used for invertible logic the most important is to create a very high quality Random Number Generator.
  These are subjects of our research
    Commercial Quantum RNG based on Hadamard Gates
    LFSR, EXOR forest, jitter generators
    FPGAs with analog-like random number generators.
FPGA realizations
Prolog Simulations
Quantum realizations of Grover Methodology
Quantum realizations of Invertible Logic with QHNN (Quantum Hopfield Neural Net)
OUR RESEARCH

## Slide 64
Generalized Oracles
Approach
Neural Networks
Quantum Neural Networks
Classical
Digital Circuit Design
Reversible
Digital Circuit Design
Quantum
Digital Circuit Design
Magnetic Spin Technology
Invertible Logic
Inverse Problems
Optimization
Problems
Constraints Satisfaction Problems
Reversible
Logic
Classical Oracle

## Slide 65: Questions often asked
How practical is this?
When we will have large quantum computers?
Error Detection and Correction.
Can we combine the powers of Invertible Logic and Reversible Logic in Quantum technology to create superior algorithms?
What is the methodology? What is the math?
  Combinatorics, coding theory, numeric representations
  Algorithms and Complexity
  Spectral Methods
  Digital Design
  Algebra, graph theory, partition theory, cube calculus theory
We do not discuss:
  Quantum Technologies
  or Magnetic Spin Technologies
I welcome any question!
Current research
No time to discuss